## Slide 1
NGT Training Department
Instructor: M.M.Naseri
Advanced Internet of Things (IoT)
Duration : 120 min

## Slide 2
NGT. Training Department
Advanced Internet of Things (IoT)
This advanced IoT course focuses on two core areas of modern IoT systems:
Network & Data CommunicationAdvanced
Firmware, Middleware & Edge Computing
The course moves beyond basic electronics and microcontroller fundamentals, focusing on reliability, scalability, security, and real-world IoT deployment.
Course Overview

## Slide 3
NGT. Training Department
Advanced Internet of Things (IoT)
Course Modules
1. Network Layer
IoT Communication ProtocolsLPWAN & Cellular NetworksIoT Network Security
Professional Firmware
ArchitectureRaspberry Pi & Remote
AccessData & Telemetry Management
OTA Updates & Maintenance
Hands-on IoT Workshop
2. Firmware & Edge Computing

## Slide 4
NGT. Training Department
Advanced Internet of Things (IoT)
Learning by Solving Real-World Problems
This course follows a Problem-Solving Approach, where engineering concepts are introduced through practical challenges.
Problem Definition: Identify the problem and system requirements.
Solution Design: Explore technologies and make engineering decisions.
Implementation: Develop and integrate hardware and software components.
Testing & Debugging: Identify issues, validate solutions, and improve reliability.
Final Product: Build a functional IoT system.
Learning Format: Conceptual explanations through presentations, followed by recorded and edited hands-on demonstrations.

## Slide 5
NGT. Training Department
Advanced Internet of Things (IoT)
Course Materials & Resources
All course materials are organized in a dedicated GitHub repository.
Course Handbook: A step-by-step guide covering practical procedures, commands, and configurations.
Practical Examples: Independent project folders containing source code and dedicated README documentation.
Presentation Slides: Course presentations will be available in the repository.
Video Demonstrations: Practical implementations, coding sessions, and hardware testing are presented in edited lesson videos.
GitHub Repository:
https://github.com/Niotx/advanced-IoT

## Slide 6
NGT. Training Department
Advanced Internet of Things (IoT)
Hardware & Development Platform
This course uses a compact set of practical hardware components for sensing, local display, embedded programming, and edge-side processing.
ESP32 DevKit V1 — Main microcontroller platform for embedded IoT development
DHT22 Sensor — Temperature and humidity sensing module
0.96" SSD1306 OLED Display — I2C display for local monitoring and feedback
Raspberry Pi 4 Model B (4GB RAM) — Edge device for communication, processing, and service hosting
These components form the core hardware platform used throughout the course.

## Slide 7
NGT. Training Department
Advanced Internet of Things (IoT)
Our Engineering Challenge
Problem Statement
An equipment room requires a smart environmental monitoring system to measure temperature and humidity, display real-time readings, and provide remote access to sensor data.
Initial Requirements
Environmental Sensing: Measure temperature and humidity using a DHT22 sensor.
Local Monitoring: Display real-time measurements on an OLED screen.
Remote Monitoring: Transmit sensor data to a Raspberry Pi over a network.
System Integration: Connect hardware, firmware, and communication components into a functional IoT system.
The Engineering Question
How can we transform a simple sensor-based device into a reliable, connected, and maintainable IoT system?

## Slide 8
NGT. Training Department
Advanced Internet of Things (IoT)
System Requirements & Initial Architecture
Before writing code, we break the engineering challenge into clear requirements and define the first system architecture.
Functional Requirements
Measure temperature and humidity
Display live readings locally
Prepare the system for future remote monitoring
Engineering Constraints
Use low-cost, available hardware
Keep the first version simple and testable
Detect invalid sensor readings- Design the firmware to be extendable
DHT22 → ESP32 → SSD1306 OLED

## Slide 9
NGT. Training Department
Advanced Internet of Things (IoT)
Hardware Integration & Wiring
The first prototype connects the sensor and display directly to the ESP32 using simple, testable wiring.
Wiring
DHT22 DATA → ESP32 GPIO4
OLED SDA → ESP32 GPIO21
OLED SCL → ESP32 GPIO22
VCC / GND → 3.3V / GND
Engineering Notes-
OLED uses I2C communication.
DHT22 uses a single data line.
A bare DHT22 may need a 10kΩ pull-up resistor.
Common OLED I2C address: 0x3C.

## Slide 10
NGT. Training Department
Advanced Internet of Things (IoT)
Reading & Displaying Sensor Data
The firmware reads environmental data from the DHT22 sensor and updates both the OLED display and Serial Monitor.
Firmware Flow
Initialize I2C, DHT22, and OLED
Read temperature and humidity
Check for invalid sensor readings
Show values on the OLED display
Print readings to Serial Monitor
Key Functions
dht.readTemperature()
dht.readHumidity()
isnan()
display.clearDisplay()
display.display()
dht.readTemperature()

## Slide 11
NGT. Training Department
Advanced Internet of Things (IoT)
Validation & Error Handling
A prototype is only useful when we can test it, detect failures, and understand what went wrong.
Validation Steps
Check OLED startup message
Verify temperature and humidity values
Compare OLED output with Serial Monitor
Disconnect the sensor and observe the error state
Error Handling
Detect invalid readings using isnan()
Show Sensor Error on the OLEDPrint error messages to Serial Monitor
Keep the system running safely
Testing failure cases is part of building an engineering product, not an optional step.

## Slide 12
NGT. Training Department
Advanced Internet of Things (IoT)
The Need for Remote Communication
Local monitoring works, but the user still needs to be physically near the device. The next engineering challenge is making sensor data accessible over the network.
Why Local Monitoring Is Not Enough
Data is only visible on the OLED
No remote access to measurements
No history or external processing
No way to connect the device to other services
Send temperature and humidity data from the ESP32 to a Raspberry Pi over the network.
Networking turns a local sensor device into a connected IoT system.

## Slide 13
NGT. Training Department
Advanced Internet of Things (IoT)
Understanding IoT Communication
Before choosing a protocol, we need to understand how devices exchange data in an IoT system.
Device to Server: ESP32 sends data directly to a server
Device to Broker: ESP32 publishes data through a message broker
Request / Response: One device asks, another responds
Publish / Subscribe: Devices communicate through topics
Should the ESP32 send data directly to the Raspberry Pi, or publish it through a communication layer?
The communication model affects scalability, reliability, and how easily other services can use the data.

## Slide 14
NGT. Training Department
Advanced Internet of Things (IoT)
MQTT vs HTTP/HTTPS vs CoAP
Different IoT protocols solve different communication problems. The right choice depends on device limits, network conditions, and data flow.
Protocol Comparison
HTTP/HTTPS: Simple request/response model, good for APIs and direct server communication
MQTT: Lightweight publish/subscribe model, ideal for continuous telemetry
CoAP: Lightweight request/response model, designed for constrained IoT devices
For this project, MQTT is the best fit because the ESP32 needs to publish sensor data continuously to a Raspberry Pi.
Protocol selection is an engineering decision, not a fixed rule.

## Slide 15
NGT. Training Department
Advanced Internet of Things (IoT)
Choosing the Right Protocol
For this project, the ESP32 needs to send small sensor readings repeatedly to a local edge device.
Decision Criteria
Low communication overhead
Continuous telemetry support
Easy data distribution to multiple subscribers
Simple integration with Raspberry Pi
Suitable for future monitoring and debugging
Use MQTT with the Raspberry Pi acting as the local broker and data receiver.
MQTT is selected because it matches our telemetry pattern, not because it is always better than HTTP or CoAP.

## Slide 16
NGT. Training Department
Advanced Internet of Things (IoT)
ESP32 vs Raspberry Pi
The ESP32 and Raspberry Pi are both used in this project, but they solve different engineering problems.
ESP32 — Microcontroller
Reads sensors directly
Controls local hardware
Runs embedded firmware
Low power and real-time oriented
ESP32 is the sensor node. Raspberry Pi is the local edge computer.
Raspberry Pi — Single Board Computer
Runs a full operating system
Hosts services like MQTT broker
Processes and stores data
Supports remote access and automation
VS

## Slide 17
NGT. Training Department
Advanced Internet of Things (IoT)
Raspberry Pi OS & SSH
To use the Raspberry Pi as an edge device, we first prepare its operating system and enable remote access.
Setup Steps
Flash Raspberry Pi OS
Configure username, password, and Wi-Fi
Enable SSH
Boot the Raspberry Pi on the local network
Connect from the Mac terminal
SSH allows us to configure and control the Raspberry Pi without connecting a monitor or keyboard.
ssh username@raspberrypi.local

## Slide 18
NGT. Training Department
Advanced Internet of Things (IoT)
Network Configuration & Secure Access
The Raspberry Pi must be reachable, stable, and protected before it can work as an IoT edge device.
Network Setup
Find the Raspberry Pi IP address
Configure a stable hostname or Static IP
Test SSH access from the Mac terminal
hostname -I
ssh username@raspberrypi.local
sudo ufw status
Secure Access
Use SSH key authentication instead of passwords
Disable root login with password
Optionally change the default SSH port
Enable ufw and close unnecessary ports

## Slide 19
NGT. Training Department
Advanced Internet of Things (IoT)
Installing the MQTT Broker
Now the Raspberry Pi becomes the local communication hub by running an MQTT broker.
Broker Setup
Install Mosquitto
Enable the Mosquitto service
Test local publish/subscribe
Prepare network access for ESP32
Keep authentication and firewall rules in mind
mosquitto_sub -t test/topic
mosquitto_pub -t test/topic -m "Hello MQTT"
sudo apt update
sudo apt install mosquitto mosquitto-clients
sudo systemctl enable mosquitto
sudo systemctl status mosquitto

## Slide 20
NGT. Training Department
Advanced Internet of Things (IoT)
MQTT Architecture
MQTT uses a broker-based architecture where devices do not communicate directly with each other.
Core Components
Publisher: ESP32 sends sensor data
Broker: Raspberry Pi receives and routes messages
Subscriber: Laptop, Python script, or dashboard receives data
Topic: Message channel, such as iot/room-01/telemetry
MQTT separates data producers from data consumers, making the system easier to extend and monitor.
ESP32 → MQTT Broker → Subscribers

## Slide 21
NGT. Training Department
Advanced Internet of Things (IoT)
MQTT QoS, Retain & Last Will
MQTT provides message delivery and status features that help make IoT communication more predictable.
MQTT Features
QoS 0: Send once, no delivery confirmation
QoS 1: At least once delivery, duplicates are possible
QoS 2: Exactly once delivery at MQTT protocol level, with more overhead
Retained Message: Broker stores the last message for a topic
Last Will: Broker publishes a status message if the device disconnects unexpectedly
iot/room-01/telemetry
iot/room-01/status

## Slide 22
NGT. Training Department
Advanced Internet of Things (IoT)
Telemetry & Message Structure
Before sending data, we need a clear message structure that describes what was measured, where it came from, and when it was created.
Use clear topic names
Include device identity
Send structured data using JSON
Add timestamps for better tracking
Keep messages small and readable
{
"device_id": "esp32-room-01",
"temperature": 24.6,
"humidity": 42.8,
"timestamp": "2026-10-03T10:30:00"
}

## Slide 23
NGT. Training Department
Advanced Internet of Things (IoT)
ESP32 MQTT Publisher
Now the ESP32 sends real sensor readings to the Raspberry Pi MQTT broker while still updating the OLED display locally.
Connect ESP32 to Wi-Fi
Connect to the MQTT broker
Read DHT22 temperature and humidity
Update the OLED display
Publish telemetry as JSON
{
"device_id": "esp32-room-01",
"temperature": 24.6,
"humidity": 42.8,
"uptime_ms": 152000
}
The ESP32 is now a real MQTT publisher, sending live environmental data to the edge device.
iot/room-01/telemetry
iot/room-01/status

## Slide 24
NGT. Training Department
Advanced Internet of Things (IoT)
Receiving & Visualizing Data
After publishing telemetry from the ESP32, we need to verify that the Raspberry Pi can receive, process, and display the data.
Receiving Methods
Use MQTT Explorer for quick message inspection
Use mosquitto_sub for terminal-based testing
Use a Python subscriber for processing telemetry
Prepare data for future dashboard visualization
mosquitto_sub -h raspberrypi.local -t iot/room-01/telemetry -u mqtt_user -P mqtt_password

## Slide 25
NGT. Training Department
Advanced Internet of Things (IoT)
Monitoring & Protocol Analysis
To debug an IoT system, we need to observe both the application messages and the network traffic.
Debugging Tools
Serial Monitor: ESP32 firmware logs
MQTT Explorer: MQTT topics and payloads
mosquitto_sub: Terminal-based message testing
Wireshark: Network packet inspection
What We Verify
ESP32 connects to Wi-Fi
Keep the system running safely
Telemetry is published correctly
Raspberry Pi receives the message
Network traffic matches the expected behavior
A reliable IoT system is built by testing, observing, and debugging each layer.

## Slide 26
NGT. Training Department
Advanced Internet of Things (IoT)
What Happens When Things Fail?
The system works in normal conditions, but an IoT product must also behave correctly when something goes wrong.
Failure Scenarios
Wi-Fi connection is lost
MQTT broker becomes unavailable
Sensor reading fails
Raspberry Pi restarts
Messages are delayed or lost
Engineering Questions
Should local monitoring continue?
Should data be buffered?
How do we detect recovery?
What should the user see?
Reliability starts by defining expected behavior during failure, not only during normal operation.

## Slide 27
NGT. Training Department
Advanced Internet of Things (IoT)
Connection Management
When the network fails, the firmware should continue running and try to recover without blocking the whole system.
Connection Strategy
Track Wi-Fi and MQTT states separatelyEnable SSH
Retry connection at controlled intervals
Keep sensor reading and OLED updates running
Publish device status when connected
Avoid infinite blocking loops
SSH allows us to configure and control the Raspberry Pi without connecting a monitor or keyboard.
Wi-Fi Connected / Disconnected
MQTT Connected / Disconnected
Sensor OK / Sensor Error

## Slide 28
NGT. Training Department
Advanced Internet of Things (IoT)
Offline Data Buffering
When MQTT is unavailable, sensor readings should not disappear immediately. The device can temporarily buffer data and publish it after recovery.
Buffering Strategy
Keep local monitoring active
Store unsent readings temporarily
Limit buffer size to protect memory
Publish buffered data after reconnection
Mark delayed data clearly
Buffering improves reliability, but it must be limited, intentional, and tested.
RAM Buffer → simple, temporary
NVS → small settings or limited records
SPIFFS/LittleFS → file-based buffering

## Slide 29
NGT. Training Department
Advanced Internet of Things (IoT)
Timestamps & Data Serialization
Sensor data becomes more useful when we know when it was measured and when it was received.
Time Tracking
uptime_ms shows time since ESP32 boot
NTP provides real network time
Measurement time and receive time are different
Delayed data must be marked clearly
Time and data format decisions affect debugging, storage, and long-term monitoring.
JSON → readable and easy to debug
MessagePack → smaller binary format
Protobuf → structured and efficient

## Slide 30
NGT. Training Department
Advanced Internet of Things (IoT)
Logging & Failure Recovery
A reliable IoT system must detect failures, record useful diagnostic information, and recover whenever possible without manual intervention.
Logging & Monitoring
Event Logging: Record important system events
Error Reporting: Identify sensor and communication failures
Log Levels: INFO, WARNING, ERROR
Remote Logging: Monitor device behavior from a central system
Failure Recovery
Automatic reconnection after network failures
Controlled retry mechanisms
Safe recovery from unexpected errors
Maintaining essential local functionality
A reliable IoT system should not only detect failures but also explain what happened and recover safely.

## Slide 31
NGT. Training Department
Advanced Internet of Things (IoT)
Firmware Architecture & Hardware Abstraction
As IoT systems grow, firmware becomes more complex. A well-structured architecture separates responsibilities, making the code easier to maintain, test, and extend.
Key Design Principles
Separation of Concerns: Divide firmware into independent functional components.
Hardware Abstraction: Separate hardware-specific operations from application logic.
Modularity: Organize code into reusable functions and modules.
Maintainability: Simplify debugging, updates, and future development.
Firmware Components
Sensor Management
Display Management
Network & MQTT Communication
Application Logic
A modular firmware architecture reduces complexity and prepares the system for more advanced designs, including FreeRTOS.

## Slide 32
NGT. Training Department
Advanced Internet of Things (IoT)
Loop-Based vs Event-Driven
Firmware tasks can be managed in different ways. Two common approaches are loop-based execution and event-driven design.
Loop-Based Approach
Tasks run repeatedly inside the main loop
Simple and easy to understand
Works well for small projects
Can become difficult to manage as complexity grows
Event-Driven Approach
Tasks respond to events, states, or scheduled triggers
Improves responsiveness and structure
Reduces unnecessary blocking behavior
Better suited for larger and more scalable systems
Common Challenge
Blocking code can delay sensor reading, display updates, and communication tasks

## Slide 33
NGT. Training Department
Advanced Internet of Things (IoT)
FreeRTOS Tasks & Queues
FreeRTOS is a real-time operating system kernel that allows embedded applications to manage multiple tasks with scheduling and inter-task communication.
Core Concepts
Tasks: Independent units of program execution
Scheduler: Manages when tasks run based on priority and readiness
Queues: Safely transfer data between tasks
Priorities: Help determine which ready task should execute first
Task Delay: Allows tasks to wait without blocking the entire system
Sensor Task → Data Queue → Display / MQTT Tasks
FreeRTOS helps organize concurrent firmware activities, while queues provide a structured way to exchange data between tasks.

## Slide 34
NGT. Training Department
Advanced Internet of Things (IoT)
Task Synchronization & Validation
Concurrent tasks must coordinate access to shared resources to prevent data corruption, unexpected behavior, and timing issues.
Synchronization Mechanisms
Mutex: Protects shared resources from simultaneous access
Binary Semaphore: Signals events between tasks
Queue: Transfers data safely between tasks
Task Priorities: Influence scheduling and responsiveness
Validation & Testing
Detect race conditions and resource conflicts
Monitor task execution and queue capacity
Test sensor failures and delayed tasks
Check for deadlocks and task starvation
Reliable multitasking requires proper synchronization, resource ownership, and systematic validation.

## Slide 35
NGT. Training Department
Advanced Internet of Things (IoT)
IoT Security Threats
Connected IoT devices introduce security risks across hardware, firmware, networks, and cloud or edge services.
Common Security Threats
Unauthorized Access: Unknown devices connect to IoT services
Eavesdropping: Unencrypted network traffic exposes sensitive data
Message Tampering: Attackers alter or inject misleading messages
Credential Exposure: Hardcoded or leaked passwords compromise devices
Device Compromise: Vulnerable firmware enables unauthorized control
Security Objectives
Confidentiality
Integrity
Authentication
Availability
IoT security must protect the entire system, not just the network connection.

## Slide 36
NGT. Training Department
Advanced Internet of Things (IoT)
Authentication & Access Control
A secure IoT system must verify device identities and restrict access to authorized resources.
Access Control Mechanisms
Authentication: Verify devices using credentials or certificates
Authorization: Define what each device is allowed to do
MQTT ACLs: Restrict publishing and subscribing by topic
Least Privilege: Grant only the permissions required
Network Protection: Limit exposed ports and services
Example Policy
ESP32 → Publish telemetry only
Python Subscriber → Read telemetry only
Authentication establishes identity; authorization controls permitted actions.

## Slide 37
NGT. Training Department
Advanced Internet of Things (IoT)
Securing MQTT with TLS
TLS protects MQTT communication against network eavesdropping and tampering while enabling the client to verify the broker's identity.
TLS Security Components
Encryption: Protects data in transit
Certificate Validation: Verifies the MQTT broker
Certificate Authority (CA): Establishes a trust relationship
Secure Transport: MQTT over TLS commonly uses port 8883
Time Validation: Requires a valid system clock for certificate checks
Secure Communication
ESP32 → TLS Connection → Mosquitto Broker
Use certificate validation and encrypted transport to protect MQTT traffic; never disable verification as a production shortcut.

## Slide 38
NGT. Training Department
Advanced Internet of Things (IoT)
Secure Provisioning & Credential Management
IoT device security depends on how credentials, certificates, and configuration data are installed, stored, updated, and revoked.
Secure Provisioning Practices
Device Identity: Assign unique identifiers and credentials
Secret Management: Keep passwords and private keys out of public repositories
Certificate Provisioning: Install only trusted certificates
Credential Rotation: Replace compromised or outdated credentials
Secure Storage: Protect sensitive data on deployed devices
Common Mistakes
Hardcoded production passwords
Shared credentials across all devices
Disabled TLS certificate verification
Exposed private keys in source control
Secure communication is only effective when device identities and credentials are managed throughout their lifecycle.